## Slide 1: CURRENT SCENARIO OF BIO-MEDICAL WASTE RULES, 2016
DR. (MRS.) JUTIKA OJAH
PROFESSOR AND HEAD,
DEPTT. OF COMMUNITY MEDICINE, GMC

## Slide 2: BIO-MEDICAL WASTE
Biomedical waste means any waste, which is generated during the diagnosis, treatment or immunization of human being or animal or research activities pertaining thereto or in the production or testing of biological or in health camps, including the categories mentioned in schedule-1 appended to BMW rules, 2016.

## Slide 4: PRESENT SCENARIO
According to the Ministry of Environment, Forest & Climate Change
Gross generation of BMW in India is 484 TPD from 168869 health care facilities, out of which 447 TPD is treated, which means that almost 38 TPD of the waste is left untreated and not disposed finding it’s way in dumps or water bodies and re-enters our system.
There are 198 CBMWF in operation and 28 are under construction.
2187o HCFs are having their own treatment facilities and 131837 HCFs are using the CBMWFs.

## Slide 5: BMW MANAGEMENT RULES 2016
SCHEDULES 1-4
FORMS 1-5
RULES 1-18

## Slide 6: BMW RULES 1998 & 2016

## Slide 7: MANDATES OF BMW RULES, 2016
These rules shall be applied to all persons who generate, collect, receive, store, transport, treat, dispose or handle bio-medical waste in any form including hospitals, nursing homes, clinics, dispensaries, veterinary institutions, animal houses, pathological laboratories, blood banks, AYUSH hospitals, clinical establishments, research or educational institutions, health camps, medical or surgical camps, vaccination camps, blood donation camps, first aid rooms in schools, forensic laboratories and research laboratories.

## Slide 8: HOW THE BMW RULES DEFINE HCF AND OCCUPIER
Health Care Facility means a place where diagnosis, treatment or immunization of human being or animal is provided irrespective of type and size of health treatment system and research activity pertaining thereto.
Occupier means a person having administrative control over the institution and the premises generating bio-medical waste, which includes a hospital, nursing home, clinic, dispensary, veterinary institution, animal house, pathological laboratory, blood bank, health care facility and clinical establishment, irrespective of their system of medicine and by whatever name they are called.

## Slide 9: SCHEDULES UNDER BMW RULES, 2016
SCHEDULE | PURPOSE/APPLICATION
SCHEDULE 1 | BMW categories and their segregation, collection, treatment, processing and disposal options
SCHEDULE 2 | Standard for treatment and disposal of BMW
SCHEDULE 3 | List of prescribed authorities and corresponding duties
SCHEDULE 4 | Label for bio-medical waste containers or bags

## Slide 10: SPECIFIED FORMS UNDER BMW RULES, 2016
FORM | MANDATES
FORM 1 | Accident reporting
FORM 2 | Application for authorization or renewal of authorization by HCF
FORM 3 | Authorization by prescribed authority
FORM 4 | Annual report by the occupier/CBMWMF operator by 30th June
FORM 5 | Appeal by the occupier to appellate authority

## Slide 11: WASTE CATEGORIES AS PER BIO-MEDICAL WASTE RULES, 2016

## Slide 12: YELLOW CATEGORY BMW
Human anatomical waste, human tissues
Animal anatomical waste, experimental animal carcasses, body parts, organs, tissues
Soiled waste, items contaminated with blood, body fluids like dressings, plaster casts, cotton swabs
Expired or discarded medicines
Chemical waste
Discarded linen, mattress, beddings contaminated with blood or body fluids

## Slide 13: RED CATEGORY BMW
Contaminated waste (recyclable)
Waste generated from disposable items such as tubing bottles, intravenous tubes and sets, catheters, urine bags.
Syringes, vaccutainers with their needles cut and gloves.

## Slide 14: WHITE CATEGORY BMW
Waste sharps including metals, needles, syringes with fixed needles, needles from needle tip cutters or burner, scalpel, blades or any other contaminated sharp object that may cause puncture and cuts. This includes both used, discarded and contaminated metal sharps.

## Slide 15: BLUE CATEGORY BMW
Glassware- broken or discarded and contaminated glass including medicine vials and ampoules except those contaminated with cytotoxic wastes, metallic body implants etc.

## Slide 16: CATEGORY WISE TREATMENT, PROCESSING AND DISPOSAL OPTIONS OF BIO-MEDICAL WASTES

## Slide 17: YELLOW CATEGORY
TYPE OF WASTE | TREATMENT AND DISPOSAL
HUMAN ANATOMICAL WASTE | INCINERATION OR PLASMA PYROLYSIS OR DEEP BURIAL
ANIMAL ANATOMICAL WASTE | 
SOILED WASTE | INCINERATION OR PLASMA PYROLYSIS OR DEEP BURIAL, (IN ABSENCE OF THESE, AUTOCLAVING OR MICRO WAVING/HYDROCLAVING FOLLOWED BY SHREDDING/ MUTILATION/ STERILIZATION AND SHREDDING. TREATED WASTE TO SENT FOR ENERGY RECOVERY).
EXPIRED OR DISCARDED MEDICINES | INCINERATION OR PLASMA PYROLYSIS AT > 1200 DEGREE CELSIUS OR ENCAPSULATION.THEN SENT BACK TO THE MANUFACTURER OR DISPOSED BY INCINERATION.

## Slide 18
TYPE OF WASTE | TREATMENT AND DISPOSAL OPTION
CHEMICAL WASTE | INCINERATION OR PLASMA PYROLYSIS OR ENCAPSULATION.
CHEMICAL LIQUID WASTE | PRE-TREATMENT BEFORE MIXING WITH OTHER WASTE WATER.
DISCARDED AND CONTAMINATED LINENS, MATTRESSES, BEDDING | NON CHLORINATED CHEMICAL DISINFECTION FOLLOWED BY INCINERATION OR PLASMA PYROLYSIS OR FOR ENERGY RECOVERY. (IN ABSENCE OF THESE, AUTOCLAVING OR MICRO WAVING/HYDROCLAVING FOLLOWED BY SHREDDING/ MUTILATION/ STERILIZATION AND SHREDDING. TREATED WASTE TO SENT FOR ENERGY RECOVERY).
MICROBIOLOGY, BIOTECHNOLOGY AND OTHER CLINICAL LABORATORY WASTE | NON CHLORINATED CHEMICAL DISINFECTION FOLLOWED BY INCINERATION.

## Slide 19: RED CATEGORY
TYPE OF WASTE | TREATMENT AND DISPOSAL OPTION
CONTAMINATED WASTE (RECYCLABLE)- WASTE FROM TUBING, BOTTLES, IV SET, CATHETERS, URINE BAGS, SYRINGES, VACCUTAINERS AND GLOVES. | AUTOCLAVING OR MICRO WAVING/HYDROCLAVING FOLLOWED BY SHREDDING/ MUTILATION/ STERILIZATION AND SHREDDING. TREATED WASTE TO BE SENT TO REGISTERED OR AUTHORIZED RECYCLERS OR FOR ENERGY RECOVERY OR PLASTICS TO DIESEL OR FUEL OIL OR FOR ROAD MAKING, WHICHEVER IS POSSIBLE.
TYPE OF BAG/ CONTAINER- RED COLOURED NON CHLORINATED PLASTIC BAGS OR CONTAINERS

## Slide 20: WHITE CATEGORY
TYPE OF WASTE | TREATMENT AND DISPOSAL OPTION
WASTE SHARPS INCLUDING METALS- NEEDLES, SYRINGES WITH FIXED NEEDLES, NEEDLES FROM NEEDLE TIP CUTTER OR BURNER, SCALPELS, BLADES, OTHER SHARP OBJECTS THAT MAY CAUSE PUNCTURE AND CUTS. THIS INCLUDES BOTH USED, DISCARDED AND CONTAMINATED METAL SHARPS. | AUTOCLAVING/ DRY HEAT STERILIZATION FOLLOWED BY SHREDDING OR MUTILATION OR ENCAPSULATION IN METAL CONTAINER OR CEMENT CONCRETE; COMBINATION OF SHREDDING CUM AUTOCLAVING AND SENT FOR FINAL DISPOSAL TO IRON FOUNDRIES OR SANITARY LANDFILL OR DESIGNATED CONCRETE WASTE SHARP PIT.
TYPE OF BAG/ CONTAINER- PUNCTURE PROOF, LEAK PROOF, TAMPER PROOF CONTAINERS

## Slide 21: BLUE CATEGORY
TYPE OF WASTE | TREATMENT AND DISPOSAL OPTION
GLASSWARE- BROKEN OR DISCARDED AND CONTAMINATED GLASS INCLUDING MEDICINE VIALS AND AMPOULES EXCEPT THOSE CONTAMINATED WITH CYTOTOXIC WASTES METALLIC BODY IMPLANTS. | DISINFECTION BY SOAKING THE WASHED GLASS WASTE AFTER CLEANING WITH DETERGENT AND SODIUM HYPOCHLORITE TREATMENT OR THROUGH AUTOCLAVING OR MICROWAVING OR HYDROCLAVING AND THEN SENT FOR RECYCLING.
TYPE OF CONTAINER- CARDBOARD BOXES WITH BLUE COLOURED MARKING

## Slide 23
All plastic bags shall be as per BIS standards.
Chemical treatment using at least 10% sodium hypochlorite having 30% residual chlorine for twenty minutes or any other equivalent chemical reagent.
Mutilation/ shredding must be to an extent to prevent unauthorized reuse.
There will be no chemical pre treatment before incineration, except for microbiological, lab and highly infectious waste.
Dead fetus below viability period can be considered as human anatomical waste.

## Slide 24
Cytotoxic drugs shall not be handed over to unauthorized person under any circumstances.
On site pre treatment of lab waste, microbiological waste, blood samples, blood bags should be disinfected or sterilized as per WHO and NACO guidelines.
Household biomedical waste during health care activities shall be segregated and handed over in separate bags to municipal waste collectors. Urban local bodies shall have tie up with the common bio medical waste treatment and disposal facility to pick up this waste from the material recovery facility or from the household directly for final disposal.

## Slide 25: THE BMW RULES, 2016 SPECIFIES THE NEED OF PRE- TREATMENT
On site pre treatment of laboratory waste, microbiological waste.
Blood samples, blood bags should be disinfected or sterilized as per the Guidelines of WHO or NACO and then given to the common bio medical waste treatment and disposal facility.

## Slide 26: SALIENT FEATURES OF BMW RULES, 2016
Duties of the occupier are elaborated.
Take all necessary steps to ensure that bio-medical waste is handled without any adverse effect to human and health and the environment in accordance with these rules.
Make a provision within the premises for a safe, ventilated and secured location for storage of segregated BMW in coloured bags or containers in the manner as specified in the Schedule 1, to ensure that there shall be no secondary handling, pilferage of recyclables or inadvertent scattering or spillage by animals and the BMW from such place or premises shall be directly transported in the manner as prescribed in these rules to the common bio-medical waste treatment facility or for the appropriate treatment and disposal, as the case may be, in the manner as prescribed in Schedule 1

## Slide 27
Pre-treat the laboratory waste, microbiological waste, blood samples and blood bags through disinfection and sterilization on site in the manner as prescribed by the WHO or NACO guidelines and then send to the common bio-medical waste treatment facility for final disposal.
Phase out use of chlorinated plastic bags, gloves and blood bags within two years from the date of notification of these rules.
Provide training to all it’s health care workers and others involved in handling of bio-medical waste at the time of induction and thereafter at least once every year and the details of training programs conducted, number of personnel trained and number of personnel not undergone any training shall be provided in the Annual Report.

## Slide 28
Immunize all it’s health care workers and others involved in handling of bio-medical waste for protection against diseases including Hepatitis B and Tetanus that are likely to be transmitted by handling of bio-medical waste, in the manner as prescribed in the National Immunization Policy or the guidelines of the Ministry of Health and Family Welfare issued from time to time.
Establish a bar code system for bags and containers containing bio-medical waste to be sent out of the premises or place for any purpose within one year from the date of the notification of these rules.

## Slide 29: GOOD BMW STORAGE SITE

## Slide 30
REPORT FOR ANY ACCIDENT AS PER BMW RULE
(AS PER FORM I OF THE RULES)
DUTY OF A HEALTH INSTITUTION AS PER BMW MANAGEMENT RULES, 2016

## Slide 31: CBMWTF RULES
BMW Rules 2016 elaborated the duties of an operator of a CBMWTF.
Operator of a common bio-medical waste treatment facility means a person who owns or controls a Common Bio-Medical Waste Treatment Facility (CBMWTF) for the collection, reception, storage, transport, treatment, disposal or any other form of handling of BMW.

## Slide 32: SERVICES TO BE PROVIDED BY THE OPERATOR OF THE CBMWTF
It shall be the duty of every operator to
Take all necessary steps to ensure that the bio-medical waste collected from the occupier is transported, handled, stored, treated and disposed of, without any adverse effects to the human health and environment, in accordance with these rules and guidelines issued by the Central Government or as the case may be the Central Pollution Control Board from time to time.
Establish bar coding system and global positioning system for handling of bio-medical waste within one year.

## Slide 33
Inform the prescribed authority immediately regarding the occupiers which are not handing over the segregated bio-medical waste in accordance with these rules.
Provide training for all it’s workers involved in handling of bio-medical waste at the time of induction and at least once a year thereafter.
Assist the occupier in training conducted by them for bio-medical waste management.
Supply non-chlorinated plastic coloured bags to the occupier on chargeable basis, if required.

## Slide 34: CYTOTOXIC WASTE
Cytotoxic waste is any material that may have come into contact with a cytotoxic drug.
Has potential to cause carcinogenic effects.
Should not be autoclaved.
Should de segregated separately.
Packaging must be labeled as cytotoxic waste.

## Slide 35
As per rules the bio medical waste bags/ containers shall have the label of Biohazard symbol

## Slide 36: STANDARDS FOR DEEP BURIAL
Unlined pit
Depth- 2 metres
Width not specified
Away from ground water sources
Shed to protect from rain water
Proper fencing.

## Slide 37: PIT MAINTENANCE
Alternate layer of BMW and soil.
Repeat daily till pit half filled.
Add lime to about 50 cm from surface.
Cover the rest with soil.

## Slide 38: THANK YOU