## Slide 1: Common Biomedical Waste Treatment Facility

## Slide 2: COMMON BIOMEDICAL WASTE TREATMENT AND DISPOSAL FACILITY
According to the Bio-medical Waste Management Rules, 2016, "bio-medical waste treatment and disposal facility" means any facility wherein treatment, disposal of bio-medical waste or processes incidental to such treatment and disposal is carried out, and includes common bio-medical waste treatment facilities
and "operator of a common bio-medical waste treatment facility" means a person who owns or controls a Common Bio-medical Waste Treatment and Disposal Facility (CBWTF) for the collection, reception, storage, transport, treatment, disposal or any other form of handling of bio-medical waste.

## Slide 3: CBWTF…
A Common Bio-medical Waste Treatment and Disposal Facility (CBWTF) is a set up where biomedical waste generated from member health care facilities is imparted necessary treatment to reduce adverse effects that this waste may pose on human health and environment. The treated recyclable waste may finally be sent for disposal in a secured landfill or for recycling .
The Bio-medical Waste Management Rules, 2016 (hereafter referred as BMWM Rules) restricts occupier for establishment of on-site or captive bio-medical waste treatment and disposal facility, if a service of common bio- medical waste treatment and disposal facility is available within a distance of seventy-five kilometre.

## Slide 4: Criteria for development of a new Common Bio-medical Waste Treatment and Disposal Facility for a locality or region.
Prepare an inventory or review by the prescribed authority under the BWM,2016.
Gap analysis w.r.to coverage area of the bio-medical waste generation and also projected over a period of next ten years, adequacy of existing treatment capacity of the CBWTF in each coverage area of radius 75 KM.
SPCB/PCC shall identify the coverage area, which require additional treatment facility and bring it to the notice of the concerned department in the business allocation of land assignment in the respective State Government or UT Administration .

## Slide 5: CBWTF
Alternately, a CBWTF may also be allowed to be established on a land procured by an entrepreneur in accordance with the location criteria suggested under these guidelines.
SPCB/PCC shall insist health care facilities to form association and to develope its own CBWTF in line with these guidelines or to have captive treatment facilities for ensuring treatment and disposal of generated bio-medical waste as stipulated under the BMWM Rules, 2016.

## Slide 6: CBWTF
In case of hilly areas considering the geography, only one CBWTF with adequate treatment capacity may be developed covering atleast two districts to cater treatment services to the HCFs located in the respective Districts. The selection and allocation of site etc., should be done as per the criteria suggested under these guidelines. The treatment charges to be prescribed by the respective SPCB/PCC in consultation with the State Advisory Committee.

## Slide 8: LOCATION CRITERIA
CBWTF shall be located near to its area of operation in order to minimize the transportation distance in waste collection, thus enhancing its operational flexibility as well as for ensuring compliance to the time limit for treatment and disposal of bio-medical waste as stipulated under the BMWM Rules (i.e., within 48 hours).
A CBWTF shall preferably be developed in a notified industrial area without any requirement of buffer zone (or)
a CBWTF shall be set up on a plot size of not less than one acre in all the areas.

## Slide 9
have minimal impact on these areas. In case of non-availability of such a land, the buffer zone distance from the notified residential area may be reduced to less than 500 m by SPCB/PCC
Sufficient land shall be allocated to the CBWTF to provide all requisite systems which include dedicated space for storage of waste (both treated and untreated), waste treatment equipment, vehicle washing bay, vehicle parking space, ETP, incineration ash storage provision, administrative room, space for DG Set etc.,.

## Slide 10: COVERAGE AREA OF CBWTF
To cater healthcare units situated at a radial distance of 75 KM. However, in a coverage area where 10,000 beds are not available within a radial distance of 75 KM, existing CBWTF in the locality (located within the respective State/UT) may be allowed to cater the healthcare units situated upto 150 KM radius w.r.to its location provided the bio-medical waste generated is collected, treated and disposed of within 48 hours as stipulated under the BMWM Rules.

## Slide 11
In case, number of beds is exceeding >10,000 beds in a locality (i.e. coverage area of the CBWTF under reference) and the existing treatment capacity is not adequate, in such a case, a new CBWTF may be allowed in such a locality in compliance to various provisions notified under the Environment (Protection) Act, 1986, to cater services only to such additional bed strength of the HCFs located.

## Slide 12: TREATMENT EQUIPMENT
a) Incineration/Plasma Pyrolysis
b) Autoclaving/Hydroclaving
c) Microwaving
d) Chemical disinfection
e) Dry heat sterilization
f) Shredder
g) Sharp pit/ Encapsulation
H)deep burial
I)NON BURN TECHNOLOGY
j) Vehicle/Containers washing facility

## Slide 13
k) Effluent Treatment Plant

## Slide 16
THANK YOU